## Slide 1
SERVER ROOM
SAFETY
IoT-Based Real-Time Monitoring & Alert System
HIT – IoT Course | Final Project |
IoT MONITORING
Students: Svetlana Gavris 342794732
Shirin Fakiri 208154815
Project Link: https://github.com/LanaGavris/IOT_SMART_HOME
Recording the presentation and running the code : https://drive.google.com/drive/u/1/folders/1HirWTi8BP8VBylFrAZ8akQzAT1fieUD0

## Slide 2
WHAT'S THE PROBLEM?
Server Room Safety · IoT Course Project · HiveMQ · MQTT · Python · SQLite
SERVER ROOM SAFETY SYSTEM
REAL-TIME IOT MONITORING & AUTOMATIC ALERTS
Do you know the temperature
in your server room right now?
Do you get notified when
the room overheats?
Do you know if someone opened
the server room door?
Do you detect smoke or
high CO2 before damage occurs?
→ If one of your answers is NO — this system is for you

## Slide 3
MAIN FEATURES
Server Room Safety · IoT Course Project · HiveMQ · MQTT · Python · SQLite
Temperature & Humidity
DHT22 sensor · every 2 sec · 4 scenarios
Smoke & CO₂ Detection
MQ-2 + MQ-135 · every 3 sec · ppm
Door Event Detection
Instant alert on any open/close event
Two Alert Levels
WARNING (elevated) and ALARM (critical)
Automatic Response
Fan + Cooling relay ON when ALARM fires
Live Data Logging
All readings stored in SQLite database
Real-Time Dashboard
GUI · live charts · color indicators
Multiple Scenarios
normal / heating / cooling / smoke / critical

## Slide 4
UNDER THE HOOD
Server Room Safety · IoT Course Project · HiveMQ · MQTT · Python · SQLite
SENSORS (Emulated in Python)
DHT22
Temperature & Humidity
MQ-2
Smoke detector (ppm)
MQ-135
CO2 / Air quality (ppm)
Door Contact
OPEN / CLOSED sensor
Fan Knob
Speed 0–100%
SOFTWARE MODULES
dht_emulator.py
— temp & humidity publisher
smoke_emulator.py
— smoke & CO2 publisher
button_emulator.py
— door & fan publisher
data_manager.py
— threshold engine + DB logger
gui_app.py
— tkinter live dashboard
config.py
— central settings (broker…)
Tech Stack: Python 3.8 | paho-mqtt | SQLite3 | tkinter | HiveMQ Public Broker

## Slide 5
HOW DOES IT WORK?
Server Room Safety · IoT Course Project · HiveMQ · MQTT · Python · SQLite
Sensors publish readings periodically via MQTT to the HiveMQ broker
Data Manager subscribes to all topics, checks thresholds, triggers alerts
If threshold exceeded — WARNING or ALARM is published + relays activated
DHT22
Temp+Humidity
MQ-2 / MQ-135
Smoke + CO2
Door Contact
Sensor
→
→
→
MQTT BROKER
(HiveMQ)
broker.hivemq.com
:1883
control commands
(fan/cooling ON)
→
Data Manager
(threshold engine
+ SQLite logger)
→
GUI Dashboard
(live view)
→
HiveMQ WebSocket
Client

## Slide 6
WORK FLOWS
Server Room Safety · IoT Course Project · HiveMQ · MQTT · Python · SQLite
SENSOR PUBLISHES TEMPERATURE EVERY 2 SECONDS
DHT22 Sensor
(temp rising)
→
serverroom_safety
_g7x2/temperature
→
MQTT BROKER
(HiveMQ)
→
Data Manager
+ SQLite DB
IF THRESHOLD EXCEEDED → ALERT PUBLISHED → RELAY ACTIVATED
Temp >= 35°C
ALARM triggered
→
alert/alarm
+ control/fan
→
MQTT BROKER
(HiveMQ)
→
Fan Relay ON
100% speed
DOOR OPEN EVENT → WARNING PUBLISHED IMMEDIATELY
Door Contact
state: OPEN
→
alert/warning
(door open)
→
MQTT BROKER
(HiveMQ)
→
GUI Dashboard
+ SQLite alert

## Slide 7
DESIGN & DEVELOPMENT STAGES
1
DEFINE REQUIREMENTS & SENSOR SELECTION
Define monitored parameters: temperature, humidity, smoke, CO2, door
Choose alert thresholds for WARNING and ALARM levels
2
DESIGN MQTT ARCHITECTURE
Define unique topic structure with project prefix
Choose HiveMQ public broker (TCP 1883 / WebSocket 8000)
3
DEVELOP PYTHON MODULES
Sensor emulators (dht, smoke, button) with realistic simulation
Data manager: threshold engine + auto-remediation + SQLite logging
GUI dashboard: live display of all sensor values
4
INTEGRATE AND TEST
Run all modules simultaneously via run_all.py
Verify alerts, relay commands, and DB logging with multiple scenarios

## Slide 8
CODE IN ACTION — SENSOR OUTPUT
Server Room Safety · IoT Course Project · HiveMQ · MQTT · Python · SQLite
dht_emulator.py --scenario heating
[DHT] HiveMQ broker: broker.hivemq.com:1883
[DHT] Scenario: heating
[DHT] Broker: OK
[DHT] tick=0000 temp=21.88C hum=45.88%
[DHT] tick=0001 temp=22.34C hum=44.59%
[DHT] tick=0020 temp=28.41C hum=43.22% <- WARNING
[DHT] tick=0047 temp=36.20C hum=41.88% <- ALARM!
smoke_emulator.py --scenario smoke
[SMOKE] Scenario: smoke
[SMOKE] Connected -> broker.hivemq.com:1883
[SMOKE] tick=0000 smoke= 42.5ppm co2= 587.3ppm
[SMOKE] tick=0001 smoke= 50.9ppm co2= 608.4ppm
[SMOKE] tick=0010 smoke= 212.0ppm co2= 1143.0ppm <- WARNING
[SMOKE] tick=0030 smoke= 516.3ppm co2= 2087.5ppm <- ALARM!
data_manager.py output
[DM] Connected -> broker.hivemq.com:1883
[DM] Sub: serverroom_safety_g7x2/temperature
[DM] Sub: serverroom_safety_g7x2/smoke ...
[ALERT] WARNING: TEMPERATURE elevated. 28.4C >= 28.0C
[ALERT] ALARM: TEMPERATURE critical! 36.2C >= 35.0C
[AUTO] -> FAN ON speed=100
[AUTO] -> COOLING ON
[ALERT] WARNING: Server room door OPEN!
[DB STATS] readings=793 warnings=18 alarms=3

## Slide 9
MQTT PAYLOADS — REAL EXAMPLES
Server Room Safety · IoT Course Project · HiveMQ · MQTT · Python · SQLite
Sensor Reading Payload
Topic: serverroom_safety_g7x2/temperature
{
"sensor": "DHT22",
"unit": "celsius",
"value": 36.2,
"tick": 47
}
ALARM Payload (alert/alarm)
Topic: serverroom_safety_g7x2/alert/alarm
{
"timestamp": "2025-05-28T10:15:32",
"level": "ALARM",
"sensor": "temperature",
"value": 36.2,
"threshold": 35.0,
"message": "ALARM: TEMPERATURE critical!"
}
Control + Door Warning
Topic: serverroom_safety_g7x2/control/fan
{\
"command": "ON",
"speed": 100
}
Topic: .../alert/warning
{
"level": "WARNING",
"sensor": "door",
"message": "Server room door OPEN!"
}
Key Code: Threshold & Auto-Remediation Logic
# data_manager.py — threshold engine
def evaluate(client, conn, sensor_type, value):
th = THRESHOLDS[sensor_type]
if value >= th["alarm"]:
level = "ALARM" # auto-remediation
if sensor_type == "temperature":
_relay(client, T["ctrl_fan"], "ON", speed=100)
_relay(client, T["ctrl_cooling"], "ON")
elif value >= th["warning"]:
level = "WARNING"
client.publish(topic, payload, qos=1)
insert_alert(conn, level, sensor_type, value, msg)

## Slide 10
RESULTS & DEMO
Server Room Safety · IoT Course Project · HiveMQ · MQTT · Python · SQLite
793
Sensor Readings
stored in SQLite
18
Warning Alerts
triggered
3
Alarm Events
detected
< 1s
Fan/Cooling
response time
HiveMQ WebSocket Demo
Connect: broker.hivemq.com Port: 8000
Subscribe: serverroom_safety_g7x2/#
See all MQTT messages in real time
How to run the demo:
python run_all.py --scenario heating
# Launches: dht_emulator, smoke_emulator,
# button_emulator, data_manager
# Temperature rises -> ALARM -> Fan ON
SQLite Database Tables:
sensor_readings (id, timestamp, sensor_type, value, unit) | device_states (id, timestamp, device, state, extra) | alerts (id, timestamp, level, sensor_type, value, message)

## Slide 11
SUMMARY AND CONCLUSIONS
Server Room Safety · IoT Course Project · HiveMQ · MQTT · Python · SQLite
Server Room Safety — IoT monitoring system for detecting temperature alerts and door events
HOW WE RESOLVED IT:
4 Python modules communicate via MQTT pub/sub — sensors publish, data manager reacts
Temperature alarm → fan + cooling automatically activated within 1 second
Door open event → WARNING alert published immediately to all subscribers
HOW WE USED THE IOT BROKER:
HiveMQ public MQTT broker — lightweight, no infrastructure required
Unique topic prefix prevents collisions on shared broker
QoS 1 ensures message delivery even under unstable connection
WebSocket port 8000 allows browser-based monitoring
Future: TLS security · Cloud DB · Mobile alerts · Grafana · Real hardware (RPi)

## Slide 12
BIBLIOGRAPHY AND SOURCES
Server Room Safety · IoT Course Project · HiveMQ · MQTT · Python · SQLite
[1]
HiveMQ Documentation — https://www.hivemq.com/docs/hivemq/
[2]
Eclipse paho-mqtt Python Client — https://pypi.org/project/paho-mqtt/
[3]
MQTT Protocol Specification v3.1.1 — https://docs.oasis-open.org/mqtt/
[4]
DHT22 Temperature & Humidity Sensor Datasheet — Aosong Electronics Co.
[5]
MQ-2 Combustible Gas Sensor Datasheet — Hanwei Electronics Co.
[6]
MQ-135 Air Quality Sensor Datasheet — Hanwei Electronics Co.
[7]
Python sqlite3 Library — https://docs.python.org/3/library/sqlite3.html
[8]
Python tkinter GUI Library — https://docs.python.org/3/library/tkinter.html
[9]
HiveMQ WebSocket Client — https://www.hivemq.com/demos/websocket-client/

## Slide 13
DESIGN & DEVELOPMENT STAGES
1
DEFINE REQUIREMENTS & SENSOR SELECTION
Define monitored parameters: temperature, humidity, smoke, CO2, door
Choose alert thresholds for WARNING and ALARM levels
2
DESIGN MQTT ARCHITECTURE
Define unique topic structure with project prefix
Choose HiveMQ public broker (TCP 1883 / WebSocket 8000)
3
DEVELOP PYTHON MODULES
Sensor emulators (dht, smoke, button) with realistic simulation
Data manager: threshold engine + auto-remediation + SQLite logging
GUI dashboard: live display of all sensor values
4
INTEGRATE AND TEST
Run all modules simultaneously via run_all.py
Verify alerts, relay commands, and DB logging with multiple scenarios